## Slide 1
Proxiant Academy
Warehouse Automation & Robotics
Week 3: Class 6

## Slide 2
Agenda
Warehouse Layout Optimization: Slotting & Zone Picking
Pick-path Optimization: TSP-based Routing
Robotic Process Automation: AMRs & Cobots
Computer Vision for Inventory Management
Digital Twin Simulation & What-if Analysis
Hands-on Lab: Pick-path Optimizer
Q&A
Proxiant Academy

## Slide 3
Warehouse Layout Optimization
Slotting optimization: Where to place SKUs?
• Demand data: Sales velocity of each product
• ABC analysis: A-products (high velocity) near packing
• Dimension-based: Large items in lower-cost high-shelves
• Picking pattern: Co-location of frequently picked items
Zone picking strategy:
• Divide warehouse into zones (e.g., 4 zones)
• Each picker responsible for 1 zone -> minimize congestion
• Reduce travel distance vs. batch picking
Proxiant Academy

## Slide 4
ABC Analysis Enhanced with ML
Traditional ABC:
• A (80% revenue): Top 20% SKUs -> High-velocity
• B (15% revenue): Middle 30% SKUs
• C (5% revenue): Low-velocity items
ML enhancements:
• Demand forecasting: Predict next month sales
• Seasonality: Adjust ABC classification by season
• Clustering: Group similar products (e.g., all beverages together)
• Recommendation: Suggest optimal shelf location
• Anomaly: Detect unusual demand spikes
Proxiant Academy

## Slide 5
Pick-path Optimization Overview
Problem: Picker has list of 30 items across warehouse
E.g., Aisle 1-Shelf 2, Aisle 3-Shelf 5, Aisle 2-Shelf 1, ...
Goal: Find shortest route visiting all locations
Related to Traveling Salesman Problem (TSP)
Algorithms:
• Nearest-neighbor: Fast, ~20% suboptimal
• 2-opt improvement: Local search to refine route
• Genetic algorithm: Evolutionary optimization
• OR-Tools TSP solver: Production-grade
Proxiant Academy

## Slide 6
Pick-path Algorithm: Nearest-Neighbor
Pseudocode:
1. Start at packing station
2. Find nearest unvisited item location
3. Move to that location, pick item
4. Repeat until all items picked
5. Return to packing station
Example: 5 items at (1,2), (5,1), (3,4), (2,5), (4,2)
Start (0,0) -> (1,2) -> (2,5) -> (3,4) -> (4,2) -> (5,1) -> (0,0)
Distance: ~16.5 units
Proxiant Academy

## Slide 7
Pick-path Optimization: 2-opt Improvement
Idea: Reverse order of route segments to reduce crossing paths
Example route: (0,0) -> (1,2) -> (2,5) -> (3,4) -> (4,2) -> (5,1) -> (0,0)
Try reversing segment (2,5)->(3,4)->(4,2):
New route: (0,0) -> (1,2) -> (4,2) -> (3,4) -> (2,5) -> (5,1) -> (0,0)
Calculate new distance, keep if better
Repeat until no improvement found
Result: Typically 10-20% better than nearest-neighbor
Proxiant Academy

## Slide 8
Wave Planning in Warehouse
Definition: Batch customer orders into waves
Wave 1 (6am-9am): 30 orders from downtown area
-> Zone picking: Zone A picks zones 1-2, Zone B picks zones 3-4
-> Sort by route -> Load vehicles in sequence
Wave 2 (9am-12pm): 25 orders from suburban area
Benefits:
• Parallel picking (multiple pickers working simultaneously)
• Efficient vehicle loading (one wave = one trailer)
• Reduced congestion vs. continuous picking
• Better utilization of dock resources
Proxiant Academy

## Slide 9
Batch Picking vs. Single-order Picking
Single-order picking:
• One picker, one customer order, walk entire warehouse
• High travel distance (~40% of cycle time)
• Example: Pick 10 items from different aisles
Batch picking:
• Group 5-10 customer orders together
• One picker walks through each location once, picks for all orders
• Use label printer to sort items post-pick
• Reduces travel distance by 50%+
• Trade-off: Requires post-pick sorting time
Proxiant Academy

## Slide 10
Autonomous Mobile Robots (AMRs)
Warehouse robots: Replace forklifts & pallet movers
Examples: Amazon Kiva (now Digit), MiR (Mobile Industrial Robots)
Goods-to-Person Systems:
• AMR transports shelf with inventory to picker station
• Picker grabs items while standing (reduced bending)
• AMR returns shelf, picks up next one
Benefits: 2-3x faster picking, reduced injury, 24/7 operation
Cost: $15k-40k per robot + fleet management software
ROI: 1-3 years for high-volume warehouses
Proxiant Academy

## Slide 11
Collaborative Robots (Cobots)
Light-payload robotic arms that work alongside humans
Examples: Universal Robots UR3/UR5, Dobot
Warehouse applications:
• Case picking: Pick cases from pallets, place on conveyor
• Palletizing: Stack cases on outbound pallets
• Depalletizing: Break down inbound pallets
• Putting away: Place items on shelves
Advantages: Flexible (quick reprogramming), safe (force-limited)
Payload: 3-10 kg, Speed: 1-2 m/sec
Cost: $35k-100k per arm
Proxiant Academy

## Slide 12
Computer Vision Applications
Barcode/QR scanning:
• Verify correct item picked (prevent picking errors)
• Handheld scanner or fixed camera at chute
Damage detection:
• CNN model to identify dented/crushed boxes
• Divert damaged items for quality control
Inventory counting:
• Drone with camera scans shelves, counts boxes
• Compare against system records -> identify discrepancies
Dimension measurement:
• 3D camera measures box size for slot allocation
• Optimize shelf configuration dynamically
Proxiant Academy

## Slide 13
Digital Twin for Warehouse Simulation
Definition: Virtual replica of physical warehouse
Tools: AnyLogic, FlexSim, SimPy (Python)
Model elements:
• Layout: Aisles, shelves, packing stations
• Entities: Orders, SKUs, pickers, AMRs
• Processes: Pick, pack, label, load
• Resources: Picker availability, dock capacity
What-if analysis:
• "If we add 1 more picker, cycle time reduces by ___?"
• "If we implement wave picking, throughput increases by ___?"
• "Optimal number of AMRs for peak demand?"
Proxiant Academy

## Slide 14
Hands-on Lab: Pick-path Optimizer (Setup)
Scenario: 15-item order in warehouse layout
Item locations (aisle, shelf, level):
Item 1: (1, 2, 1), Item 2: (3, 1, 2), Item 3: (2, 4, 1), ...
Packing station: (0, 0)
Algorithm: Nearest-neighbor + 2-opt improvement
Metrics:
• Total walking distance
• Pick cycle time (estimated 20 sec/item + travel)
• Number of aisles traversed
Proxiant Academy

## Slide 15
Lab: Python Implementation
import math
def distance(p1, p2):
return math.sqrt((p1[0]-p2[0])**2 + (p1[1]-p2[1])**2)
def nearest_neighbor(start, items):
route = [start]
unvisited = set(range(len(items)))
while unvisited:
nearest = min(unvisited, key=lambda i: distance(route[-1], items[i]))
route.append(items[nearest])
unvisited.remove(nearest)
return route + [start]
Proxiant Academy

## Slide 16
Lab: 2-opt Improvement Implementation
def two_opt(route, items):
improved = True
while improved:
improved = False
for i in range(1, len(route)-2):
for j in range(i+1, len(route)-1):
new_route = route[:i] + route[i:j][::-1] + route[j:]
if total_distance(new_route) < total_distance(route):
route = new_route
improved = True
break
return route
Proxiant Academy

## Slide 17
Key Takeaways
Warehouse optimization is multi-layer: Layout -> Picking -> Packing
ABC analysis guides slotting; ML improves classification
Pick-path optimization (TSP) reduces picking time by 20-40%
Robotics (AMRs, cobots) increase throughput & reduce injuries
Computer vision prevents errors & counts inventory automatically
Digital twins enable risk-free scenario analysis before implementation
Hands-on: Built 15-item pick path in ~5 minutes with nearest-neighbor + 2-opt
Proxiant Academy

## Slide 18
Proxiant Academy
www.proxiant.com
Master AI. Professionally.