## Slide 1
Proxiant Academy
Predictive Maintenance with AI
Week 4: Class 7

## Slide 2
Agenda
Condition Monitoring: Sensors & Feature Extraction
Remaining Useful Life (RUL) Prediction
Anomaly Detection Techniques
Maintenance Scheduling Optimization
P-F Curve & Failure Modes Analysis
Hands-on Lab: RUL Prediction with NASA Data
Q&A
Proxiant Academy

## Slide 3
Condition Monitoring: Sensor Types
Vibration analysis:
• Accelerometer measures vibration signature
• FFT (Fast Fourier Transform) extracts frequency content
• Feature: Peak frequency, RMS, crest factor -> detect imbalance, misalignment
Temperature trending:
• Infrared or contact thermometer
• Baseline: Normal operating temp, Alert: +20C above baseline
Oil analysis (for engines):
• Iron/copper particles: Bearing wear
• Viscosity change: Contamination or degradation
Acoustic emission:
• Ultrasonic sensor detects crack propagation
Proxiant Academy

## Slide 4
Vibration Feature Extraction: FFT
Raw vibration signal: 10,000 samples at 10 kHz sampling rate (1 second)
Apply FFT: Transform time-domain -> frequency-domain
Frequency range: 0-5 kHz (Nyquist frequency)
Extract features:
• Peak frequency: 1.5 kHz (indicates imbalance)
• Power spectral density at bearing defect frequency (BPFO)
• Broadband noise floor: Indicates wear/spalling
Example: Bearing defect frequency = 5 * (rpm/60)
If rpm=3000, BPFO=250 Hz -> Look for 250 Hz spike
Proxiant Academy

## Slide 5
Remaining Useful Life (RUL) Prediction
Definition: Time until equipment fails (in days/operating hours)
Challenge: Equipment behavior is complex, failures are rare
Approaches:
1. Survival analysis (statistical)
2. Machine learning regression
3. Deep learning (LSTM)
Goal: Predict equipment will fail in 30 days -> Schedule maintenance before failure
Benefit: Avoid catastrophic failures, reduce downtime
Cost savings: Maintenance cost << unplanned failure cost
Proxiant Academy

## Slide 6
Survival Analysis: Kaplan-Meier Estimator
Concept: What % of equipment is still functioning at time T?
Kaplan-Meier survival curve:
• Track 100 identical machines for 5 years
• At 1 year: 95 still working (5% failed)
• At 2 years: 85 still working (10 more failed)
• At 5 years: 40 still working
Use for: Warranty periods, maintenance scheduling
Cox Proportional Hazards model:
• Include covariates (operating load, temperature, hours)
• Estimate hazard ratio for each covariate
Proxiant Academy

## Slide 7
ML for RUL: Random Survival Forest
Algorithm: Ensemble of survival trees
Library: scikit-survival (Python)
Training data:
Features: [mileage, age, temp_avg, vibration_rms, oil_iron_ppm]
Target: (time_to_failure, failure_occurred [0/1])
Example training row:
[45000 km, 3 years, 85C, 2.5 mm/s, 180 ppm] -> (45 days to failure, failure=1)
Prediction: Equipment with [50000, 2.5, 90, 3.2, 250] -> 25 days to failure
Actionable: Schedule maintenance within 25 days
Proxiant Academy

## Slide 8
Deep Learning for RUL: LSTM Networks
Challenge: Degradation is sequential, non-linear
LSTM (Long Short-Term Memory): Captures temporal dependencies
Architecture:
Input: Sequence of [vibration_rms, temp, pressure] over 30 days
LSTM layer: 64 units
Dense layer: Predict RUL (days to failure)
Output: Single value (e.g., 18 days)
Advantage over Random Forest:
• Captures degradation trajectory
• Better for non-stationary sensor data
• Can use full time-series history
Proxiant Academy

## Slide 9
Anomaly Detection: Statistical Methods
CUSUM (Cumulative Sum Control Chart):
• Monitor deviation from baseline
• Alert if cumulative sum exceeds threshold
• Good for trending (gradual increase in temp)
EWMA (Exponentially Weighted Moving Average):
• Weight recent observations more heavily
• Smooth short-term noise, detect longer-term drift
• Formula: EWMA = a*X + (1-a)*EWMA_prev, (a=0.1-0.3)
Threshold: Alert if EWMA > baseline + 3*std_dev
Proxiant Academy

## Slide 10
Anomaly Detection: ML Approaches
Isolation Forest:
• Isolate anomalies by random partitioning
• Non-anomalies need many partitions, anomalies need few
• Multivariate: Detect unusual combinations of sensors
• Example: Normal if (temp=80, vibration=2.0), Anomaly if (95, 4.5)
Autoencoder (Neural Network):
• Encoder: Compress sensor stream -> low-dim representation
• Decoder: Reconstruct original signal
• Anomaly: High reconstruction error
• Good for: detecting new failure patterns not in training data
Proxiant Academy

## Slide 11
P-F Curve: From Symptom to Failure
P-point: Potential failure (first detectable symptom)
• Vibration spike appears, but equipment still works
• Detected by alarm threshold in condition monitoring
F-point: Functional failure (equipment can no longer do job)
• Equipment fails catastrophically
P-F interval: Time between P and F
• Bearing: P-F = 1-2 weeks
• Pump seal: P-F = 2-4 weeks
• Goal: Detect at P, schedule maintenance before F
Strategy: Set alarm at P, give technician P-F interval to fix
Proxiant Academy

## Slide 12
Failure Modes & Degradation Patterns
Bearing failures:
• Spalling: Progressive surface wear -> accelerating vibration
• Raceway crack: Sharp impulsive vibration peaks
• Cage fracture: Noise increases unpredictably
Seal leakage:
• Pressure drop: Linear degradation (predictable)
• Sudden rupture: Nonlinear (difficult to predict)
Valve erosion:
• Flow rate decreases gradually (smooth degradation)
• Erosion accelerates at high pressure/temperature
Feature engineering goal: Extract features specific to each failure mode
Proxiant Academy

## Slide 13
Hands-on Lab: NASA Turbofan RUL (Setup)
Dataset: NASA C-MAPSS (Commercial Modular Aero-Propulsion System Simulation)
• 100+ simulated turbofan engines, operated to failure
• Features: 21 sensors (temperature, pressure, speed, flow rate)
• Target: Cycles to failure (RUL in cycles)
Example row:
Engine_ID | Cycle | Sensor1 (temp) | Sensor2 (pressure) | ... | RUL
1 | 1 | 100.0 | 518.67 | ... | 191
1 | 2 | 100.0 | 518.67 | ... | 190
...
1 | 191 | 106.5 | 624.35 | ... | 0
Proxiant Academy

## Slide 14
Lab: Data Preparation Step-by-Step
# 1. Load data
train_df = pd.read_csv("train_FD001.txt", header=None)
# Columns: [engine_id, cycle, sensor1, sensor2, ..., sensor21]
# 2. Create RUL column
train_df["RUL"] = train_df.groupby(0).cumcount(ascending=False) + 1
# 3. Normalize sensor values (0-1 scale)
from sklearn.preprocessing import MinMaxScaler
scaler = MinMaxScaler()
sensor_cols = list(range(2, 23))
train_df[sensor_cols] = scaler.fit_transform(train_df[sensor_cols])
Proxiant Academy

## Slide 15
Lab: Extract Features for RUL Prediction
# Rolling statistics over last N cycles
def create_features(data, window=10):
features = []
for i in range(window, len(data)):
# Mean of last N cycles
means = data.iloc[i-window:i, 2:23].mean()
# Std dev
stds = data.iloc[i-window:i, 2:23].std()
# Trend (linear regression slope)
trend = np.polyfit(range(window), data.iloc[i-window:i, 2], 1)[0]
features.append(np.concatenate([means, stds, [trend]]))
return np.array(features)
Proxiant Academy

## Slide 16
Lab: Train Survival Forest Model
from sksurv.ensemble import RandomSurvivalForest
from sksurv.util import Surv
# Prepare training data
X_train = engineered_features
y_train = Surv.from_arrays(
event=(train_df["RUL"] == 0),
time=train_df["RUL"]
)
# Train model
rsf = RandomSurvivalForest(n_estimators=100, random_state=42)
rsf.fit(X_train, y_train)
# Predict RUL
predictions = rsf.predict(X_test)
Proxiant Academy

## Slide 17
Key Takeaways
Condition monitoring: Vibration (FFT), temperature, oil analysis, acoustics
RUL prediction combines survival analysis + ML (Random Forest) + DL (LSTM)
P-F curve: Detect symptom at P, fix before failure at F
Anomaly detection: CUSUM/EWMA (statistical) vs. Isolation Forest/Autoencoder (ML)
Failure modes differ: Bearing spalling (accelerating) vs. seal leakage (linear)
Hands-on: NASA C-MAPSS turbofan RUL prediction using survival forest
Next: Apply to real equipment with 6-12 months historical data
Proxiant Academy

## Slide 18
Proxiant Academy
www.proxiant.com
Master AI. Professionally.