## Slide 1
Proxiant Academy
AI-Powered Quality Control
Week 4: Class 8

## Slide 2
Agenda
Statistical Process Control (SPC) & Control Charts
Computer Vision for Defect Detection
Root Cause Analysis with AI
Six Sigma + AI Integration
Quality Prediction & Soft Sensors
Hands-on Lab: Defect Detection with Transfer Learning
Q&A
Proxiant Academy

## Slide 3
Statistical Process Control (SPC)
Definition: Monitor process variation to detect anomalies early
Key concepts:
• Common cause variation: Natural process noise (acceptable)
• Special cause variation: Assignable defect (investigate)
Control limits:
• UCL (Upper Control Limit) = Mean + 3*StdDev
• LCL (Lower Control Limit) = Mean - 3*StdDev
• Action: If point outside UCL/LCL -> Stop, investigate, fix
Charts: X-bar (mean), R (range), p (proportion defective), c (count defects)
Proxiant Academy

## Slide 4
Control Chart Types & Usage
X-bar chart (subgroup mean):
• Product: Bottle weight, bolt diameter, paint thickness
• Interval: Measure 5 items every hour, plot mean
R chart (subgroup range):
• Detects consistency (variability) changes
• R = Max - Min of subgroup
p chart (proportion defective):
• Counted data: % defective units in batch
• Example: 100 units inspected, 2 defective -> p=0.02
c chart (defect count):
• Count defects per unit (e.g., surface scratches per car door)
Proxiant Academy

## Slide 5
Western Electric Rules for SPC
Rule 1: Single point outside 3-sigma limits -> Out of control
Rule 2: 2 of 3 consecutive points beyond 2-sigma limits -> Trend
Rule 3: 4 of 5 consecutive points beyond 1-sigma limits -> Drift
Rule 4: 8 consecutive points on same side of center line -> Shift
Rule 5: 6 consecutive points steadily increasing/decreasing -> Trend detected
Example application:
Detect process degradation before product goes out of spec
Alert supervisor -> Adjust temperature, flow, pressure
Proxiant Academy

## Slide 6
ML-Enhanced SPC: Adaptive Limits
Traditional SPC: Fixed control limits (static)
Problem: Doesn't account for changing operating conditions
ML enhancement:
Input: Historical quality data + operating conditions (temp, pressure, line speed)
Model: Random Forest predicts expected quality variance
Output: Adaptive control limits based on current conditions
Example:
High speed (500 units/min): Wider limits (more variation)
Low speed (200 units/min): Tighter limits
Reduces false alarms while detecting real issues
Proxiant Academy

## Slide 7
Computer Vision Defect Detection
Challenge: Inspect 1000+ products/hour manually - not feasible
Solution: Camera + CNN model inspects 100% of production
Defect types:
• Surface scratches: Texture variation in images
• Dimensional errors: Bounding box too small/large
• Color mismatch: Pixel RGB values outside range
• Missing component: Segmentation misses expected region
• Contamination: Foreground objects (dust, hair) detected
Setup: Camera at end of production line, real-time processing (<1 sec/image)
Reject defective units -> Automated diverter
Proxiant Academy

## Slide 8
CNN Architectures: ResNet & EfficientNet
ResNet-18 (Residual Networks):
• 18 layers with skip connections
• Prevents vanishing gradient problem
• Good for: Texture defects, surface anomalies
• Parameters: 11M, Speed: 10ms per image (GPU)
EfficientNet-B0:
• Scaled for efficiency (4M parameters vs ResNet)
• Faster inference on edge devices (Jetson, RPI)
• Good for: Real-time production lines, limited compute
Transfer learning: Use ImageNet pre-trained weights, fine-tune on defect images
Proxiant Academy

## Slide 9
YOLO: Real-time Object Detection
YOLO (You Only Look Once): Single-pass detection network
Use case: Detect multiple defect locations on single product
Example: PCB (circuit board) with 5 solder joint defects
Output: [x, y, width, height, class, confidence] for each defect
Speed: YOLOv5s = 50ms per 640x640 image (GPU)
Accuracy: 92% mAP on custom defect dataset
Implementation: OpenCV + YOLOv5 + Python
1. Capture image from camera
2. Pass to YOLO model
3. Draw bounding boxes, classify defect severity
4. Trigger reject if confidence > 0.8
Proxiant Academy

## Slide 10
Transfer Learning for Defect Detection
ImageNet: Pre-trained on 14M images, 1000 classes
Strategy: Reuse learned features (edges, textures, shapes)
Step 1: Load ResNet-18 pre-trained on ImageNet
from torchvision import models
model = models.resnet18(pretrained=True)
Step 2: Replace final layer for defect classification
model.fc = nn.Linear(512, 2) # [normal, defective]
Step 3: Freeze early layers, fine-tune on defect images (~500 images)
• Prevents overfitting
• Converges in 10-20 epochs
Result: 95% defect detection accuracy with minimal labeled data
Proxiant Academy

## Slide 11
Root Cause Analysis: Causal Inference
Question: Did temperature increase CAUSE the defect spike?
Traditional correlation: Doesn't prove causation
DoWhy library (Python): Causal inference framework
1. Define causal graph: Temperature -> Equipment Wear -> Defects
2. Adjust for confounders (age, maintenance history)
3. Estimate causal effect: "1C increase -> X% more defects"
Bayesian Networks:
• Graph: Temperature -> Viscosity -> Friction -> Wear -> Defects
• Infer: Given defect observed, what caused it?
• Probability: P(Temperature too high | Defect detected) = 0.8
Proxiant Academy

## Slide 12
Automating Root Cause: 5-Why Analysis
Traditional 5-Why (manual, error-prone):
1. Why defect? -> Solder joint cold
2. Why cold solder? -> Soldering iron too cool
3. Why cool? -> Thermostat broken
4. Why not fixed? -> Maintenance backlog
5. Why backlog? -> Staff shortage
AI-assisted 5-Why:
• NLP processes technician notes: "Solder joint failed inspection"
• Query knowledge base: Common causes of solder failures
• Suggest 5 most likely root causes ranked by probability
• Guide technician through diagnosis tree
Proxiant Academy

## Slide 13
Six Sigma + AI: DMAIC Framework
DMAIC: Define -> Measure -> Analyze -> Improve -> Control
AI role in each phase:
Define: NLP analyzes customer feedback -> priority metrics
Measure: Automated data collection from sensors/cameras
Analyze: Statistical tests + ML finds top drivers of defects
Improve: Optimization (genetic algorithm) suggests setpoints
Control: ML-enhanced SPC with adaptive limits
Goal: Reduce defect rate to 3.4 ppm (Six Sigma = ±6 sigma)
Proxiant Academy

## Slide 14
Soft Sensors: Predict Quality Without Direct Measurement
Challenge: Direct measurement is slow/expensive
Example: Tensile strength test destroys sample (destructive test)
Soft sensor: Infer property from easily-measured inputs
Inputs: [temperature, pressure, line speed, humidity]
Model: Neural network trained on historical data
Output: Predicted tensile strength in real-time
Benefits: 1000s/day predictions vs. 10/day destructive tests
Accuracy: Within 5% of actual (validated on holdout samples)
Application: Adjust process to hit target property before product ships
Proxiant Academy

## Slide 15
Hands-on Lab: Defect Detection with Transfer Learning (Setup)
Dataset: Electronics PCB (Printed Circuit Board) defects
• 500 normal PCB images (224x224)
• 500 defective images (solder bridges, missing components, cold joints)
Task: Binary classification (normal vs. defective)
Pipeline steps:
1. Data prep: Augmentation (rotation, flip, zoom)
2. Model: ResNet-18 transfer learning
3. Training: Fine-tune on PCB data
4. Evaluation: Accuracy, precision, recall, F1 score
5. Deployment: Real-time inspection on production line
Proxiant Academy

## Slide 16
Lab: ResNet-18 Transfer Learning Code
import torch, torch.nn as nn, torchvision.models as models
from torch.optim import Adam
# Load pre-trained ResNet-18
model = models.resnet18(pretrained=True)
for param in model.parameters():
param.requires_grad = False
# Replace final layer
model.fc = nn.Linear(512, 2)
# Training loop
optimizer = Adam(model.fc.parameters(), lr=0.001)
criterion = nn.CrossEntropyLoss()
for epoch in range(20):
for images, labels in train_loader:
outputs = model(images)
loss = criterion(outputs, labels)
loss.backward()
optimizer.step()
Proxiant Academy

## Slide 17
Key Takeaways
SPC monitors variation; control charts detect special causes
Western Electric rules detect trends/shifts before out-of-spec
Computer vision (CNN, YOLO) inspects 1000+ units/hour @ 95%+ accuracy
Transfer learning: Reuse ImageNet weights, fine-tune with 500 defect images
Root cause analysis: Causal inference + NLP automates 5-Why process
Six Sigma + AI: ML enhances every DMAIC phase
Soft sensors: Predict unmeasured properties in real-time
Hands-on: ResNet-18 defect detector trained in 20 epochs, ready for production
Proxiant Academy

## Slide 18
Proxiant Academy
www.proxiant.com
Master AI. Professionally.