## Slide 1
Proxiant Academy
Resource Allocation & Scheduling
Week 5 | Class 10
Proxiant Academy

## Slide 2
Agenda
Job Shop Scheduling Problem & Formulation
Constraint Programming vs Mixed-Integer Programming
Google CP-SAT Solver: Core Concepts
Workforce Optimization & Shift Scheduling
Capacity Planning & Demand Matching
Energy Optimization & Smart Grid Integration
Hands-On Lab: Production Scheduling with CP-SAT
Proxiant Academy

## Slide 3
Job Shop Scheduling Problem
Definition: assign jobs to machines, minimize total time
n jobs, m machines, each job has task sequence
Constraints: precedence, machine availability, capacity
Objective: minimize makespan (max completion time)
NP-hard: exact solvers needed for real problems
Google CP-SAT: state-of-art constraint programming solver
Proxiant Academy

## Slide 4
Job Shop Example: 10 Jobs, 3 Machines
Job 1: Task A (Machine 1, 5min) → Task B (Machine 2, 3min)
Job 2: Task C (Machine 2, 4min) → Task A (Machine 1, 6min)
Job 3: Task B (Machine 3, 2min) → Task C (Machine 2, 5min)
... (10 jobs total)
Find: schedule that minimizes total time while respecting
machine availability and task dependencies
Proxiant Academy

## Slide 5
Constraint Programming vs MIP
MIP (Mixed-Integer Programming): formulate all constraints algebraically
Pros: mature solvers (CPLEX, Gurobi)
Cons: large problem size → slow, limited by formulation
CP (Constraint Programming): declarative, flexible constraints
Pros: handles complex logic, efficient search strategies
Cons: less proven for some problem classes
Winner for scheduling: CP excels with disjunctive constraints
Proxiant Academy

## Slide 6
Google OR-Tools & CP-SAT
pip install ortools
CP-SAT combines:
Constraint propagation: fast feasibility checking
MIP relaxation: lower bounds
Local search: near-optimal solutions
Multi-core: parallelizes search automatically
Proxiant Academy

## Slide 7
CP-SAT: Variables & Constraints
Variables: IntVar for discrete values, IntervalVar for time windows
task = model.NewIntervalVar(start, duration, end, name)
Constraints: NoOverlap, AddDisjunctive, AddCumulative
precedence: model.Add(task1_end <= task2_start)
resource: model.AddNoOverlap([task1, task2]) for same machine
capacity: model.AddCumulative(tasks, capacities)
Proxiant Academy

## Slide 8
Code: Define Objective & Solve
makespan = model.NewIntVar(0, 1000, 'makespan')
model.Add(makespan >= all_end_times)
model.Minimize(makespan)
solver = cp_model.CpSolver()
solver.parameters.log_search_progress = True
status = solver.Solve(model)
print(f'Makespan: {solver.Value(makespan)}')
Proxiant Academy

## Slide 9
Code: Job Shop Model in CP-SAT
for job_id, job in enumerate(jobs):
for task_id, (machine, duration) in enumerate(job):
start = model.NewIntVar(0, 1000, f'J{job_id}T{task_id}_start')
task = model.NewIntervalVar(start, duration, start+duration, ...)
for other_job: add precedence constraints
add_to_machine_list[machine]
for machine_tasks: model.AddNoOverlap(machine_tasks)
Proxiant Academy

## Slide 10
Gantt Chart Visualization
X-axis: time, Y-axis: machines
Each job represented as colored bar
Bar position: start/end time
Gaps indicate idle time or waiting
Tools: matplotlib, plotly, dash
Example: visualize optimal schedule from CP-SAT solution
Proxiant Academy

## Slide 11
Workforce Optimization: Shift Scheduling
Problem: assign workers to shifts, meet coverage demand
Variables: worker-shift assignments (binary: yes/no)
Constraints: skill requirements, max hours, break times
Objective: minimize labor cost while meeting demand
Fairness: balance workload across workers
ML integration: demand forecasting → shift planning
Proxiant Academy

## Slide 12
Skill-Based Resource Assignment
Task requires specific skill set (e.g., 'welding', 'quality_inspection')
Workers have skill profiles: [(skill, proficiency_level)]
Assignment: match worker skills to task requirements
Constraint: can only assign if worker has skill level >= required
Objective: minimize cost or maximize throughput
Dynamic: retraining improves skill availability
Proxiant Academy

## Slide 13
Labor Demand Forecasting
Input: historical workload, seasonal patterns, future demand
Method: time series forecasting (ARIMA, Prophet, LSTM)
Output: predicted labor hours needed per week/day
Schedule optimization: adjust shift plans based on forecast
Feedback: monitor actual vs predicted → retrain model
Result: reduced overtime, better service levels
Proxiant Academy

## Slide 14
Capacity Planning: Demand-Capacity Matching
Demand: forecasted customer orders, MPS (master production schedule)
Capacity: available machine hours, worker shifts, material supply
Gap analysis: identify periods of over/under-capacity
Actions: adjust batch sizes, work schedules, outsourcing
Simulation: test scenarios (hiring, equipment purchase, process speed)
Proxiant Academy

## Slide 15
Energy Optimization: Peak Demand & Renewables
Load scheduling: shift energy-intensive tasks to low-cost periods
Time-of-use pricing: electricity cheaper off-peak (e.g., night)
Constraint: schedule production without exceeding grid peak
Renewable integration: prioritize solar/wind when available
Smart grid: real-time price signals → dynamic scheduling
Objective: minimize energy cost + carbon footprint
Proxiant Academy

## Slide 16
HANDS-ON LAB: Production Scheduling with CP-SAT
Scenario: 10 jobs across 3 machines, 5-10min task durations
Step 1: Define jobs, tasks, machines in data structure
Step 2: Create CP-SAT model, add variables & constraints
Step 3: Solve and retrieve makespan, job completion times
Step 4: Generate Gantt chart visualization
Bonus: Add skill-based resource constraint
Proxiant Academy

## Slide 17
Key Takeaways
CP-SAT solver: powerful for scheduling & allocation problems
Constraint formulation crucial: clear constraints = faster solution
Workforce + capacity + energy optimization are interconnected
Gantt charts: essential for communication & validation
Practical: scheduling can reduce costs 10-20% in real operations
Next: MLOps deployment & monitoring for AI systems
Proxiant Academy

## Slide 18
Questions & Discussion
Proxiant Academy